## Slide 1: Vegetation Dynamics from NDVI Time Series Analysis at Carmel Valley
Jeff Yen
Department of Geography, San Diego State University
#RemoteSensing #changedetection #VEGEtationDYNAMics

## Slide 2: Project Motivation
Remote sensing (RS) imagery has been most commonly used to conduct LULC change analysis because of the ability to observe landscape across regions in a synoptic and timely.
Vegetation is the majority of land covers on earth, understanding vegetation dynamics is important to promote our lives in many perspectives (e.g., urban planning and management).
Previous research on vegetation dynamics primarily emphasizes on the area of vegetation change, though the few focuses on the speed of vegetation change.

## Slide 3: Project Objectives
To provide more comprehensive aspects of vegetation dynamics based on three indicators:
  Vegetation NDVI value change
  Speed of vegetation NDVI value change
  Acceleration of vegetation NDVI value change
To automate image processing routines via Python 2.7 and ArcPy

## Slide 4: Data
Four images (2010, 2012, 2014, 2016) were collected from National Agriculture Imagery Program (NAIP) using Google Earth Engine (GEE).
The collected NAIP images have the following characteristics:
  Spatial resolution: 1 m
  Spectral resolution: R, G, B, NIR
  Radiometric resolution: 8-bit unsigned (0 – 255)

## Slide 5: Methods
The entire image processing routine is divided into three parts:
  Reading image information from .csv file
  Classifying vegetation
    Binary vegetation classification based on given NDVI thresholds
  Performing vegetation dynamics based on NDVI time-series change detection
    Vegetation NDVI value change: T1(2012-2010), T2(2014-2012), T3(2016-2014)
    Speed of vegetation NDVI value change: S1:(T2-T1)/2, S2:(T3-T2)/2
    Acceleration of vegetation NDVI value change: A1: (S2-S1)/2

## Slide 6: Method – Cont.
The following ArcPy methods were adopted to complete certain stage of this project:
  arcpy.GetParameterAsText
  arcpy.env.workspace
  arcpy.CheckOutExtension
  arcpy.AddMessage
  arcpy.Raster
  arcpy.GetRasterProperties_management
  arcpy.sa
    Int
    Float
    SetNull
    RemapRange
    Reclassify

## Slide 7: Reading image information from .csv file
Attribute in .csv file:
Time-efficient user input and great reusability

## Slide 8: Reading image information from .csv file – cont.
<= Get image resolution from user, either 30m or 1m
<= read and append image information into lists
(i.e., image path, time stamp, ndvi threshold)
<= Calculate the number of image input to iteratively classify vegetation and execute NDVI time-series change detection
skip the first row, which is the each field name

## Slide 9: Classifying vegetation
<= iteratively classify vegetation and append NDVI time-series to a list
<= Calculate NDVI

## Slide 10: Classifying vegetation – Cont.
<= Classify Vegetation and create binary vegetation classification map

## Slide 11: Performing NDVI time-series change detection
<= input parameters for change detection
<= calculate three indicators for NDVI time-series change detection

## Slide 12: ResultS

## Slide 13: Vegetation Classification
2010
2012
2014
2016

## Slide 14: Summary of Vegetation Classification
Year | Vegetation Coverage (m^2) | Percentage of Vegetation Coverage (%)
2010 | 45423760 | 16.1
2012 | 32251308 | 11.4
2014 | 20784488 | 7.4
2016 | 14123916 | 5.0

## Slide 15: Vegetation NDVI Value CHANGE
T1: 2012-2010
T2: 2014-2012
T3: 2016-2014
Time | Avg. VEG_NDVI Value Change | Std. VEG_NDVI Value Change
T1 (2012 - 2010) | 13.55 | 10.68
T2 (2014 - 2012) | 7.54 | 11.73
T3 (2016 - 2014) | -20.08 | 9.86

## Slide 16: The Speed of Vegetation NDVI Value CHANGE
S1: (T2-T1)/2
S2: (T3-T2)/2
Time | Avg. Speed of VEG_NDVI Value Change | Std. Speed of VEG_NDVI Value Change
S1:(T2-T1)/2 | -5.73 | 8.93
S2:(T3-T2)/2 | -13.41 | 9.69

## Slide 17: The Acceleration of Vegetation NDVI Value CHANGE
A1: (S2-S1)/2
Time | Avg. Acceleration of VEG_NDVI Value Change | Std. Acceleration of VEG_NDVI Value Change
A1:(S2-S1)/2 | -8.94 | 13.03

## Slide 18: Limitations, Challenges and Problems
Limitations:
  Subjective NDVI threshold
  Per-pixel-based classification
Challenges:
  Reduce computational time of 1m NAIP images
  Compact the python script
  Difficulty in appropriately visualizing the results
Problems:
  Unable to incorporate third-party python libraries unless setting global environment in Windows OS.

## Slide 19: Thank You!!
Contact: cyen@sdsu.edu
Q&A